Condition Inspection - N437RP

Date: ________

Remove all inspection panels and aircraft interior prior to starting inspection

	Cabin side panels (4),							

	Pressure controller in rear seat bottom,

	Baggage compartment panels (6) and upholstery,

	Two inspection panels and two flap actuator cover panels on each wing.

	Trim servo panels optional if servo tests OK

	Winglets (contain wiring, AOA and fuel system connections)

	Upper and lower cowling

	Prop spinner

	Cabin door inner cover and latch covers

	Pilot and copilot seats (check seat tracks (4) for proper latching on ALL tracks)

Fuselage/Cabin

	Panel/skin delamination; cracks anywhere (esp rear fuselage & tail; and around pressure vessel)

	Windows-cracks or delamination from mounting surfaces

	Water drain holes in bottom of fuselage (2), rudder (1) and wings (1 each)

	Winglet fuel vents-functional

	Fuselage drain holes (3), rudder (2), wings/speed brakes (1 each wing)

	Emergency survival gear and critical spares in baggage compartment

	Emergency door opening tools in glove compartment

	Pitot & Static system leak check (every two years)

	Oxygen bottle pressure & masks serviceable (4); check regulator and flow

	Halon fire extinguisher-Underside/back of copilot seat-charged and serviceable

	Transponder check (every two years)

	Radios & Intercom –all functional

	Rear seat intercoms

	ELT-Functional Check/Battery replaced as required (inside tail access panel)

	Chelton and Garmin data systems-functional, with current data loads

Propeller

	Run-out and balance

	Bearing wear & grease seals

	Air conditioner compressor belt-condition

Critical fasteners re-torqued

	Fuselage motor mount bolts (5) (40'/lb)

	Engine mount bolts (4) (40'/lb)

	Propeller nuts (6) (80-85'/lb)

	Wing spar bolts (2 rear spar bolts@40'/lb; 2 main spar bolts@40'/lb)

	Nose and MLG attachment and linkage bolts-all

	Nose gear over-center pivot bolts-torque and verify free pivot on bushing (SB077-0518)

	Flight control mounting -all

Flight Controls

	Control system binding/travel limits & stops

	Continuity, lubrication and excess free play--each connector/each pivot; end to end

	Autopilot servo attachments /assembly bolts & screws/over-center lockouts

	All control system linkage-aileron, elevator, rudder pivots for tightness and wear

	Flap operating linkage

	Flap tracks; dry lube

Hydraulic System

	Hydraulic reservoir -fluid level per dipstick marking

	Accumulator pre-charge--test via flap extension/retraction with electrical system off

	Brake reservoir -fluid level (engine compartment; left upper side of firewall)

	MLG, nose gear and flap actuators for leaks, binding

	MLG actuator area for security of hidden bolts/fasteners (mirror required!)

	MLG mechanical down locks for proper functioning of lockdown pins

	All hoses & tubing fitting ends, especially under rear seat bottom and wheel well area

	Hydraulic system filter (front side of right wheel bulkhead)

Lubrication:

	Wheel bearings-repack & adjust bearing pre-load

	MLG rack & pinion gears/steel sliders

	MLG pivot bearings-hard to access/important to lube

	Gear door hinges & latches

	Front seat tracks

	Nose gear operating linkage & pivot bearings

	Cabin door hinges & latches

	Flight Control bearings & operating linkage (LOTS of them!)

	Engine Operating Controls-Throttle/Mixture/Prop

Electrical System

	Bus Tie functions

	Emergency Power relay

	#1 & #2 battery load tests

	#2 charging system regulator set 0.2 volts below #1 system to "load" the primary system

	Battery replacement

	Exterior position lighting/strobes

	Landing and taxi lights

	Cockpit/instrument lighting

	Replace 9 volt emergency glare shield light battery (top side of fuse panel; above copilot knees)

	Replace button battery in ELT activation switch-right side of instrument panel

	Test back-up battery in Garmin 696

	Test back-up battery in Dynon D-10A

	Glare shield lighting

	Caution and warning lights (6)-lamp test and proper operation of each

	Cockpit emergency lights: flashlight between seats/mini on glare shield/hand-held in glove box

	Replace small batteries: fuse panel, baggage compartment, O2 sensors, rear headphones

	Emergency Comm radio back of CP seat) recharged/tested

	Pitot heat and "on" indicator light

	Speed brake operation (pilot position only)

	Trim-elevator, aileron and rudder all drive to limits/reverse/operate from both sticks

Fuel System

	Gascolator cleaned

	Fuel tank caps for function and sealing

	Wing fuel sumps checked (4)

	Selector valve-detents noticeable/off position stops gas flow

Landing Gear

	Gear extension, down-lock & door closing; test-on jacks

	MLG door nylon sliders for wear/delamination

	Wheel well compartments for chafing, wiring security

	Brake line condition--especially where it exits the top of the MLG leg

	Gear "down" and "in-transit" micro-switches (2 on each gear leg) -check for good condition

	Tire tread-reverse/replace tires/tubes

	Tires serviced to 65/45/65 PSI

	Brake pads-within wear limits (0.100" min thickness)

	Brake line weep hole in MLG strut clear and clean (no brake fluid leaks)

	Bolts securing MLG axles to base and aluminum bases to steel MLG tubes

	All bolts securing nose gear assembly; torque bolts (2) between upper/lower nose gear drag links

	Nose gear drag links--critical: lift nose, disconnect gas spring and check for over-center flex

	Nose strut extension: 3" min of polished strut showing (service to 300 PSI when fully extended)

Engine Compartment

	Air seals around upper cowling

	Engine air inlet bypass for free operation and warning light

	Air filter- replace

	All SCEET for cracks & tears

	Condition of induction air flex tubes (2)

	Condition of wiring & hoses behind engine (multiple opportunities for mischief here!)

	Engine mount for cracks…especially at welds (critical item)

	Lubricate operating controls-all

	Shim motor mounts to raise engine spinner (as required)

Engine Checks:

	Oil cooler for cracks in mounting flanges; air door for proper operation

	Compression/80: #1-      ; #2-      ; #3-      ; #4-      ; #5-      ; #6-      z

	Sparkplugs-clean/replace or re-gap (30-36 #/ft tightening torque)

	Borescope inspection of each cylinder (pix and/or notes on valve condition; each cyl)

	Fuel Injectors-clean (injectors are number-matched to each cylinder)

	Oil & Filter-replace

	Fuel system calibration IAW Continental M 01

	Boost pump (high/low)

	Replace or overhaul mags @ 500 hours

	Slick Mag inspection -- Slick Service Bulletin SB3-08

	Magneto Timing: each at 24 degrees BTDC (Must use protractor on prop spinner)

	Magnetos (L & R) grounding check

	Oil lines-condition/leaks/chafing; find the source of ANY oil leaks-fix

	Intake manifold gaskets for leaks

	All intake and turbo feed hose clamps tightened

	Exhaust system-condition & pressure test for cracks (inc V clamps per SAIB CE-13-45)

Cabin Air System

	Cabin door pressure seal-no leaks/holds pressure

	Cabin door to door frame electrical contacts - cleaned/adjusted

	Cabin pressurization controller –operation & filter replacement

	Cabin heat, defroster & dump controls

	Cabin fan

Air Conditioner

	Condenser fans, exhaust scoop and airflow sequencing valves

	Water drain in pressure controller "potty"

	Refrigerant leaks, especially in rear fuselage area

	Operating pressure check, R134A (min of 120 psi, normal day, not running)

	Cabin seat belts/shoulder harness/attach points-all functional, good condition

Ground checks (engine running)

	Engine and aircraft instrument controls (operation and limits)

	Magneto Grounding (engine shut down using ignition switch)

	Fuel selector Shut-Off (engine shut down using fuel selector-Off)

	Compass headings (Chelton and Dynon)

	Taxi straight ahead/brakes steer aircraft easily

Flight Checks

	Engine gauges (operation and limits)

	Prop governor operation

	Take Off power (@DA 2200’; Temp 90F): RPM:       MP:         ; FF:         ; Fuel Press:      PSI

	In-flight Mags check (L & R) under high power setting

	Emergency nose gear extension speed w/hydraulic pressure depleted:         KIAS (130 KIAS min)

	Gear manual extension:         strokes w/hand pump

	Chelton “fast erect” in-flight

	Autopilot tracking, stability and dampening checks

	Cabin pressure monitoring and alerting system (should alarm at 10,000')

	Fuel pump warning system (should flag the boost pump not on above 14,000')

	AOA warning system

Paperwork

	Airworthiness Directives

	Lancair Service Bulletins

	Airworthiness certificate

	Operating limitations letter

	Aircraft data plate (fuselage near tail)

	Registration certificate (applied for new with Texas address)

	Log book entries for proper documentation

	Compass correction card-on instrument panel

	Weight & Balance-available & conforms to equipment installed